# Conveyor station

# Exercise 4: Using sensors

## Learning objectives

Upon completing this exercise, you should

be familiar with the mode of operation and range of applications of opto and inductive sensors

be able to incorporate the sensors into circuit diagrams

be able to read the sensors in the conveyor station using FluidSIM®

## Problem description

Sensors are used in automated systems to monitor the status of the system. The conveyor station uses so-called proximity sensors that are most often used to detect the presence or position of objects.

## Task

Connect the opto and inductive sensors to the multi-pin plug distributor of the conveyor station. Connect the EasyPort to the multi-pin plug distributor and to the power supply. The sensors are now functional. This is indicated by the LEDs on the sensors and/or multi-pin plug distributor. Bring various objects close to the sensors and study their behaviour. Mark in the table the objects to which the sensor responds. What else do you notice? What could the sensors be used for?

In FluidSIM®, create a circuit where the sensors switch on a lamp when activated.

## Aids

Theory book

FluidSIM® online help

Data sheets

Conveyor station

Picture of the station

Name:							Class:			Date:

- Connect the opto and inductive sensors to the multi-pin plug distributor of the conveyor station. Connect the EasyPort to the multi-pin plug distributor and to the power supply. The sensors are now functional. This is indicated by the LEDs on the sensors and/or multi-pin plug distributor. Bring various objects close to the sensors and study their behaviour. Mark in the table the objects to which the sensor responds. What else do you notice? What could the sensors be used for?

| Object | Opto sensor | Inductive sensor |
| --- | --- | --- |
| Red workpiece |  |  |
| Black workpiece |  |  |
| Silver workpiece |  |  |
| Coin |  |  |
| Finger |  |  |
| Paper |  |  |

In FluidSIM®, create a circuit where the sensors switch on a lamp when activated.