# Conveyor station

# Exercise 6: Learning about logic operations

## Learning objectives

Upon completing this exercise, you should

be familiar with the most important logic operations

be able to create logic programs in FluidSIM®

be able to solve simple control tasks using logic operations

## Problem description

Logic operations are an important basis of control technology. In the FluidSIM® logic module, inputs and outputs are linked using logic operations. This exercise deals with the most important logic operations.

## Task

Transfer the following logic circuits to FluidSIM® and study the circuit's behaviour by setting the input channels I1 through I3 to the status 'high' by clicking on them. Complete the truth table. In each case specify an example of a control task that can be solved using this logic operation.

Create the logic circuit shown below in FluidSIM®, test its behaviour and describe it. What control tasks can this so-called latching element be used for?

Create the circuit shown below in FluidSIM®.
Open the logic module and create a program with the following characteristics:
•	Lamp P1 should light up when the two pushbuttons T1 and T2 are pressed (and stay on
	after pushbuttons T1 and T2 have been released).
•	The lamp should switch off when pushbuttons T3 or T4 are actuated.

Extend the circuit from Exercise 3 so that an electric motor is switched on and off instead of the lamp.

## Aids

Theory book

FluidSIM®

FluidSIM® online help

Name:							Class:			Date:

- Transfer the following logic circuits to FluidSIM® and study the circuit's behaviour by setting the input channels I1 through I3 to the status 'high' by clicking on them. Complete the truth table. In each case specify an example of a control task that can be solved using this logic operation.

|  | I1 I2 I3 Q1 0 0 0 0 0 1 0 1 0 0 1 1 1 1 1 1 1 0 1 0 1 1 0 0 |
| --- | --- |

Example of a control task:

|  | I1 I2 I3 Q1 0 0 0 0 0 1 0 1 0 0 1 1 1 1 1 1 1 0 1 0 1 1 0 0 |
| --- | --- |

Example of a control task:

Name:							Class:			Date:

|  | I1 Q1 0 1 |
| --- | --- |

Example of a control task:

|  | I1 I2 Q1 0 1 0 1 1 1 1 0 |
| --- | --- |

Example of a control task:

Name:							Class:			Date:

Create the logic circuit shown below in FluidSIM®, test its behaviour and describe it. What control tasks can this so-called latching element be used for?

Name:							Class:			Date:

Create the circuit shown below in FluidSIM®.

Open the logic module and create a program with the following characteristics:
•	Lamp P1 should light up when the two pushbuttons T1 and T2 are pressed (and stay on
	after pushbuttons T1 and T2 have been released).
•	The lamp should switch off when pushbuttons T3 or T4 are actuated.

Name:							Class:			Date:

Extend the circuit so that an electric motor is switched on and off instead of the lamp.