# Conveyor station

# Solution to exercise 1: Learning about components and their function

## Learning objective

Upon completing this exercise, you should

be familiar with the most important components in the conveyor station

## Problem description

All automated systems use a range of components such as sensors, valves, motors, etc. It is important to be familiar with the function of the components in a system.

## Task

Match the components with their correct designation and describe their purpose within the station.

## Aids

Theory book

FluidSIM® online help

Data sheets

Name:							Class:			Date:

- Match the components with their correct designation and describe their purpose within the station.

| No. | Designation | Function within the station |
| --- | --- | --- |
| 1 | Opto sensor | Senses whether there are workpieces at the start of the conveyor |
| 2 | DC geared motor | Allows the conveyor to advance or reverse |
| 3 | Relays | Control the DC motor |
| 4 | Multi-pin plug distributor | Provides the electrical connection for the sensors and actuators |
| 5 | Solenoid | Rejects workpieces onto the slide |
| 6 | Inductive sensor | Senses metal workpieces |
| 7 | Slide | Stores rejected workpieces |
| 8 | Cable duct | For neat installation of cables |