# Conveyor station

# Solution to exercise 3: Learning about the structure of symbols

## Learning objectives

Upon completing this exercise, you should

be familiar with the symbol and designation of key pneumatic components

be familiar with the structure of the symbols

## Problem description

All automated systems use a range of components such as sensors, valves, motors, etc. It is important to describe the function of the system clearly and simply. This is achieved using, among other things, electrical, pneumatic and hydraulic circuit diagrams.

To understand these circuit diagrams, you must be familiar with the symbols used. This exercise is designed to teach you about the symbols.

## Task

- Shown below are a number of circuit symbols. Enter the name of the component as well as the description of the numbered symbols in the tables.

## Aids

Theory book

FluidSIM® online help

Data sheets

Name:							Class:			Date:

- Shown below are a number of circuit symbols. Enter the name of the component as well as the description of the numbered symbols in the tables.

|  | Name of the component |
| --- | --- |
|  | Inductive proximity sensor, inductive sensor |
|  | Function of the symbols |
|  | 1 24 V connection 2 0 V connection 3 Signal output 4 Symbol for electronic sensor 5 Symbol for N/O contact 6 Symbol for inductive sensor |

|  | Name of the component |
| --- | --- |
|  | Pushbutton (N/O contact) |
|  | Function of the symbols |
|  | 1 24 V connection 2 0 V connection 3 Symbol for pushbutton (N/O contact) |

Name:							Class:			Date:

|  | Name of the component |
| --- | --- |
|  | Switch (N/O contact) |
|  | Function of the symbols |
|  | 1 24 V connection 2 0 V connection 3 Symbol for switch (N/O contact) |

|  | Name of the component |
| --- | --- |
|  | Relay |
|  | Function of the symbols |
|  | 1 24 V connection 2 0 V connection 3 N/O contact (actuated by a coil) 4 Coil 5 24 V connection 6 0 V connection |