# Handling station

# Exercise 7: Creating control systems via sequencing programs

## Learning objective

Upon completing this exercise, you should

be familiar with the mode of operation and fields of application of sequencing

be able to create simple control systems via sequencing programs

## Problem description

Many sequences in automation technology are characterised by one process step having to take place after another. Sensors check whether one step has been successfully completed before the next step starts. This is referred to as sequencing. There is a special programming technique available for user-friendly sequencing.

A simple sequence is to be programmed that lifts a workpiece in the handling station from the holder using the vertically arranged cylinder. The workpiece should then be released again when a pushbutton is actuated.

## Task

Read up about the programming technique for sequencing in the theory section. Describe the basic idea in your own words.

Create a schematic diagram of the setup as well as an allocation list that shows which electrical components are plugged into which slots on the multi-pin plug distributor. Also create the pneumatic and electrical circuit diagrams in FluidSIM® (using the logic module, still without a program).

Describe in detail the sequence outlined in the problem description. Use the prepared form on the worksheet.

Open the logic module in FluidSIM® by clicking on it with the mouse and create the program to accomplish the sequence described in Exercise 3. Test the program via simulation.

Test the program using the handling station. Ensure that the wiring and the tubing correspond to the circuit diagram and assignment list.

## Aids

Theory book

FluidSIM®

Handling station

Name:							Class:			Date:

- Read up about the sequencing programming technique in the theory section. Describe the basic idea in your own words.

Create a schematic diagram of the setup as well as an allocation list that shows which electrical components are plugged into which slots on the multi-pin plug distributor. Also create the pneumatic and electrical circuit diagrams in FluidSIM® (using the logic module, still without a program).

Schematic diagram

Name:							Class:			Date:

| Slot | Designation | Explanation |
| --- | --- | --- |
| 4 |  |  |
| 6 |  |  |
| 5 |  |  |
| 7 |  |  |

Name:							Class:			Date:

Describe in detail the sequence outlined in the problem description. Use the prepared form on the worksheet.

| Schritt | Aktion | Ausgang | Bedingung |
| --- | --- | --- | --- |
| 0 |  |  |  |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |

Open the logic module in FluidSIM® by clicking on it with the mouse and create the program to accomplish the sequence described in Exercise 3. Test the program via simulation.

Name:							Class:			Date:

Test the program using the handling station. Ensure that the wiring and the tubing correspond to the circuit diagram and allocation list.