# Handling station

# Solution to exercise 4: Creating schematic and circuit diagrams

## Learning objective

Upon completing this exercise, you should

be able to create schematic diagrams, pneumatic circuit diagrams and allocation lists

## Problem description

Engineers use schematic diagrams, technical drawings, part lists or circuit diagrams to represent machines or machine parts efficiently and clearly.

## Task

Create a schematic diagram for the handling station pictured, showing the function and position of the key components.

Create an allocation list that specifies which sensor or actuator is plugged into which slot on the multi-pin plug distributor.

Create a pneumatic circuit diagram of the station using FluidSIM®.

## Aids

Theory book

FluidSIM®

Handling station

Picture of the station

Name:							Class:			Date:

- Create a schematic diagram for the handling station pictured, showing the function and position of the key components.

Create an allocation list that specifies which sensor or actuator is plugged into which slot on the multi-pin plug distributor.

| Slot | Designation | Description |
| --- | --- | --- |
| 0 | 1S1 | Magnetic proximity sensor at cylinder 1A, rear |
| 2 | 1S2 | Magnetic proximity sensor at cylinder 1A, front |
| 4 | 2S1 | Magnetic proximity sensor at cylinder 2A, top |
| 6 | 2S2 | Magnetic proximity sensor at cylinder 2A, bottom |
| 1 | 1M1 | Advance cylinder 1 |
| 3 | 1M2 | Retract cylinder 1 |
| 5 | 2M1 | Advance cylinder 2 |
| 7 | 2M2 | Retract cylinder 2 |
| 9 | 3M1 | Close gripper |

Name:							Class:			Date:

Create a pneumatic circuit diagram of the station using FluidSIM®.