# Stacking magazine station

# Exercise 7: Controlling using relays

## Learning objectives

Upon completing this exercise, you should

be familiar with the mode of operation and fields of application of relays

be able to create simple control systems using relays

be able to realise logic operations using relays

be able to realise circuits using time relays

## Problem description

Relays are one of the most important components in modern control systems, even and particularly in the age of microelectronic controllers.

## Tasks

- Read up about the structure and mode of operation of relays.
What types of relay are you familiar with?

In FluidSIM®, create an actuator for a solenoid coil using a pushbutton and a relay.

Two-hand start devices are often used for safety reasons. This means that a machine can only start if two pushbuttons are actuated simultaneously. The purpose of this device is to prevent the machine operator from sticking a hand into the machine while it is running. Create a circuit for a two-handed start device of a single-acting cylinder. Test the circuit in the FluidSIM® simulation mode. Could this function also be realised using switches?

Many processes are time-controlled. The press-in unit of the stacking magazine station should press together the container and lid for exactly 10 s to allow an adhesive to cure. Develop a control system for this on the basis of the circuit from Exercise 1. Test your circuit via simulation and using the stacking magazine station.

## Aids

Theory book

FluidSIM®

Name:							Class:			Date:

- Read up about the structure and mode of operation of relays.
What types of relay are you familiar with?

In FluidSIM®, create an actuating circuit for a solenoid coil using a pushbutton and a relay. 
Do this by adding to the circuit diagram shown below.

Name:							Class:			Date:

Two-hand start devices are often used for safety reasons. This means that a machine can only start if two pushbuttons are actuated simultaneously. The purpose of this is to prevent the machine operator from sticking a hand into the machine while it is running. Create a circuit for a two-handed start device of a single-acting cylinder. Test the circuit in the FluidSIM® simulation mode. Could this function also be realised using switches?

Name:							Class:			Date:

Many processes are time-controlled. The press-in unit of the stacking magazine station should press together the container and lid for exactly 10 s to allow an adhesive to cure. Develop a control system for this on the basis of the circuit from Exercise 1. Test your circuit via simulation and using the stacking magazine station.