# Stacking magazine station

# Solution to exercise 1: Learning about components and their function

## Learning objective

Upon completing this exercise, you should

- be familiar with the most important components used in the stacking magazine station

## Problem description

All automated systems use a range of components such as sensors, valves, motors, etc. It is important to be familiar with the function of the components in a system.

## Task

Match the components with their correct designation and describe their purpose within the station.

## Aids

- Theory book

- FluidSIM® online help

- Data sheets

Name:							Class:			Date:

- Match the components with their correct designation and describe their purpose within the station.

| No. | Designation | Function within the station |
| --- | --- | --- |
| 1 | One-way flow control valve | Regulates the speed of the cylinders |
| 2 | Single-acting cylinder | Presses the cover into the socket |
| 3 | Storage plate | Holds workpieces |
| 4 | Multi-pin plug distributor | Provides the electrical connection for the sensors and actuators |
| 5 | 4/2-way double solenoid valve | Actuates the double-acting cylinder |
| 6 | 4/2-way single solenoid valve | Actuates the single-acting cylinder |
| 7 | Double-acting cylinder | Pushes the workpieces out of the magazine |
| 8 | Magnetic proximity sensor | Outputs a signal as soon as the piston of the double-acting cylinder passes the sensor |
| 9 | 3/2-way hand valve | Shuts off the compressed air supply |
| 10 | Cable duct | Routes the cables |
| 11 | Magazine | Stacks the workpieces |