# Stacking magazine station

# Solution to exercise 8: Using proximity sensors

## Learning objectives

Upon completing this exercise, you should

- be familiar with the function of magnetic proximity sensors

- be able to realise control circuits using sensors

- be able to create simple sequencers

## Problem description

Sensors are an important part of all automated systems. The stacking magazine station features a magnetic proximity sensor that detects the position of a cylinder piston.

A control system is to be developed for the stacking magazine with the following characteristics:

- The operator places a container in the assembly device and pushes the Start button.

- The double-acting cylinder pushes a lid out of the storage tower (onto the container) and then returns to its normal position.

- The single-acting cylinder presses together the container and lid for exactly 10 s.

- The operator removes the finished workpiece (container plus lid).

- The colour of the container and lid should be immaterial.

## Tasks

- How can you ensure that the single-acting cylinder only advances when the double-acting cylinder is fully advanced? What component is required?

Create a schematic diagram of the setup.

Create an electropneumatic circuit in FluidSIM® and test it via simulation. Create an allocation list for the inputs and outputs of the multi-pin plug distributor.

Set up the station as per the schematic diagram, install tubing between all pneumatic components and connect the electrical components to the multi-pin plug distributor. Test the function of the control system using the station.

## Aids

- Theory book

- FluidSIM®

Name:							Class:			Date:

- How can you ensure that the single-acting cylinder only advances when the double-acting cylinder is fully advanced? What component is required?

There are magnetic proximity sensors for this function. These detect the position of the cylinder piston. The cylinder piston contains a permanent magnet that activates the proximity sensor. The signal can be used to actuate the following steps.

Alternatively, the presence of the lid can be sensed by means of a through-beam sensor (this could be borrowed from the conveyor station).

An inductive sensor is also an option if only metal lids are used.

Circuit symbol for the magnetic sensor

Create a schematic diagram of the setup.

Note: Your schematic diagram can vary slightly; however, the arrangement of the components must be clear.

Name:							Class:			Date:

Create an electropneumatic circuit in FluidSIM® and test it via simulation. Create an allocation list for the inputs and outputs of the multi-pin plug distributor.

| Slot | Assignment | Function |
| --- | --- | --- |
| 0 | 1S1 | Proximity sensor at cylinder 1 |
| 1 | 1M1 | Solenoid coil 1 at valve 1 (advance cylinder 1A) |
| 3 | 1M2 | Solenoid coil 2 at valve 1 (retract cylinder 1A) |
| 5 | 2M1 | Solenoid coil 1 at valve 2 (advance cylinder 2A) |

Set up the station as per the schematic diagram, install tubing between all pneumatic components and connect the electrical components to the multi-pin plug distributor. Test the function of the control system using the station.